## Slide 1
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 1 of 14
Page 1
What Is MachinePilot?
Prepare products, configure machine accessories, and review process simulations on your computer.
Parts
Prepare geometry and accessory relationships
Product
Create a board, panel, or carrier
Recipe
Configure the machine, then plan and simulate processing
What do you start with?
What do you review at the end?
Notes: {"使用者母版頁": 1, "原教材頁": 1, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "第一頁兼封面，以一張情境圖說明本課用途、對象與預期成果。", "未補齊證據": [], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 2
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 2 of 14
Page 2
Starting Data and Checks
Prepare the product data, BOM, and component database before starting.
Check the task data
Compare the Gerber data and work instructions or component list. Check components, part numbers, reference designators, and board locations.
What the template provides
Check the board structure, workpart properties, fiducials, and positioning method. Identify existing data and missing information.
Confirm readiness
Check component-to-accessory relationships and machine data. Select the same saved product when creating the recipe.
Scope of the examples
The examples use Demo_Single_Board, Demo_Panel_Board, or Demo_Carrier_Board.
Reference
Part Number
Description
C52
495-2473-3-ND
Metallized polyester film capacitor; 10 nF, ±10%, 100 V DC / 63 V AC
C172
ESK107M050AG3EA
Polarized aluminum electrolytic capacitor; 100 μF, ±20%, 50 V DC; 2,000 h at 85°C; −40 to 85°C
D01
EP1WSS6R2J
Surge-resistant wirewound resistor; 6.2 Ω, ±5%, 1 W; ±400 ppm/°C; −55 to 155°C
RY1
835-1A-F-V
PCB power relay; SPST-NO, Class F insulation, sealed; coil approximately 0.45 W; 240 V AC / 10 A resistive load
Component Part Numbers
Component List
Notes: {"使用者母版頁": 2, "原教材頁": 2, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "一張圖帶出BOM、元件、裝載與機台條件的困難。", "未補齊證據": [], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 3
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 3 of 14
Page 3
MachinePilot Training Kit
Step 1 of 2
1
Course Story
2
Basics
The Challenge
The Solution
Progress from a single board and a new part number to a panel and two products on a carrier.
Expected Outcome
Choose suitable product and setup methods.
Explain the simulation results.
Notes: {"使用者母版頁": 3, "原教材頁": 3, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用解法圖說明元件→產品→Recipe、配置與模擬的關係，吸收Workflow概念。", "未補齊證據": ["G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 4
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 4 of 14
Page 4
Four Scenarios and Today's Learning Goals
Step 1 of 2
1
Course Story
2
Basics
Scenario 1: Single Board
Use four prepared components to complete product creation and automatic
recipe planning.
Scenario 2: New Part + Front Feed
Reuse existing geometry for a new part number, update annotations, and
restrict feeder placement.
Scenarios 3 and 4: Panel and Carrier
Compare panel processing modes, create carrier products, and plan
recipes independently.
3D Concept Illustration
Notes: {"使用者母版頁": 4, "原教材頁": 4, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "同頁呈現四情境路線與辨識問題、選擇方法、完成並驗證成果的目標。", "未補齊證據": [], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 5
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 5 of 14
Page 5
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Object Tree
Properties and 3D View
Read the selected object's data and check its geometry and position.
Messages and Results
Check save, setup, and simulation messages.
Locate the product, board, geometry link, and annotations. Select the correct
object before editing.
Menu
Menus: Workspace, Electronic Component, Product, Recipe, Database Management,
About, Manual. Each opens its own tools.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 6
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 6 of 14
Page 6
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Workspace
  Reset Workspace: Clear the current project.
  Exit: Close the application.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 7
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 7 of 14
Page 7
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Electronic Component
  New Component: Create from geometry (later).
    New from Template: Create from a template (later).
    Deep Clone from Asset: Copy a component and its related assets. Set the database group and part number. Used in this course.
  Open Project: Choose a database group and component.
  Save to Library: Save the component and settings to its group.
  Component Relations: Set tool/feeder links (advanced).
  Scene Roles: Set simulation roles (advanced).
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 8
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 8 of 14
Page 8
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Product
  New Board: Create a single board.
  New Panel: Panel; cross-board or whole-panel planning.
  New Carrier: Carrier; cross-board planning only.
  Open Project: Select a product.
  Save to Library: Save to the database group.
  Measure: Check X, Y, Z distances.
    Origin to feature: Click the floor, then the feature.
    Feature to feature: Click the start, then the end feature.
  Payload Preview: Load 3D models; check footprint alignment.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 9
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 9 of 14
Page 9
Object Selection and Parent–Child Hierarchy
Course Guide
Step 2 of 2
1
Course Story
2
Basics
Start at the correct level
The board and its parent panel or carrier each have their own workpart and positioning data.
Match the tree to the view
Select a node and check its corresponding geometry in the 3D view before editing.
Identify what you are changing
Distinguish between editing a board, a geometry link, and the complete product.
Menu
Notes: {"使用者母版頁": 6, "原教材頁": 6, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "串起樹節點與3D選取、父子層級及確認操作對象。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 10
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 10 of 14
Page 10
Focus and Inspect the 3D View
Course Guide
Step 2 of 2
1
Course Story
2
Basics
Focus on the work object
Right-click the node and select Focus Viewport
/ Fit Board to view the board from above.
Rotate the view
Point at the object. Hold the mouse
wheel and move to rotate the
view. Compare this with pointing at
the floor.
Pan the view
The viewpoint changes the view only. Move Board / Move
Geometry Link changes the object's position.
Menu
Notes: {"使用者母版頁": 7, "原教材頁": 7, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "同頁示範聚焦、縮放、旋轉與適用的顯示操作，區分視角與模型移動。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 11
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 11 of 14
Page 11
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Recipe
  Follow the workflow below:
    Project Creation
      Create Project
      Open Project
    Product Assembly
      Select Position: Set the product flow direction, from right to left or the reverse.
      Adjust Orientation: Rotate the product to match its actual working orientation.
      Select Attachment Point: Select a feature to connect the product to the machine. Hide the machine or conveyor as needed to improve visibility.
      Conveyor Width: Adjust the width as a reference for setting the physical conveyor.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 12
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 12 of 14
Page 12
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Recipe
    Machine Capability Assessment
      Slot: Configure from the machine assembly perspective.
        Auto Configuration: Use the button at the upper right to plan according to locks and the current configuration.
        Lock: Preserve the current slot setting. An empty slot stays empty; an occupied slot retains its accessory. These constraints are passed to the algorithm.
        Enable: Control slot use in the current layout for machine readback.
      Product: Configure from the component perspective.
        Specify the feeder, tool, and installation position for each component.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 13
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 13 of 14
Page 13
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Recipe
    Flow Editor: Adjust the generated process:
      Round
      Feeder slot
      Tool slot
      Pick sequence
      Insert sequence
    Algorithm Settings
        Consistent Planning Result: True by default; use consistent planning preferences.
        Prioritize Components: Prefer shorter parts first. Database integration is under verification.
        Time Constrain: Standard sets the planning time for a recipe result.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 14
DIATwin MachinePilot Training Kit
Course Guide and Basic Operations
Page 14 of 14
Page 14
Explore the Workspace
Step 2 of 2
1
Course Story
2
Basics
Menu
Recipe
    Simulation
      Cycle Time: Available after simulation finishes.
      CHECK COLLISION: Check interference during downward Move actions.
      Move*** [Entry/Target/Place/Exit]: Algorithm-generated pick/place commands. Click a command to move the model immediately to that position.
      Grasp Pose: Select a different tool grasp pose (advanced).
      Offset: Adjust a point where interference occurs.
      START / RESET: Start or reset the simulation.
      EXPORT DB: Generate the D30 machine recipe.
Notes: {"使用者母版頁": 5, "原教材頁": 5, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用介面全貌圖指認物件樹、屬性、3D視窗與訊息區，示範各區用途。", "未補齊證據": ["G-UI"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}