## Slide 1
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 1 of 20
Page 15
Scenario 1: Task and Preparation
Step 1 of 5
1
Prepare
2
Parts
3
Product
4
Recipe
5
Results
Source Materials
Prepare Demo_Single_Board, APEX Gerber,
BOM_APEX.csv, and APEX_Bom.xlsx.
Demo Designators and Starting Data
Use RY1, C172, D01, and C52. Match BOM designators,
part numbers, and geometry before annotation.
Save the product; auto-configure the recipe. Check collisions, simulate, and record cycle time.
Notes: {"使用者母版頁": 9, "原教材頁": 9, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "一頁交代任務與Demo_Single_Board、四料BOM／零件表、Gerber、機台及配件，區分已備妥與待完成項目。", "未補齊證據": ["QS01-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 2
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 2 of 20
Page 16
Quick Start: From Annotation to Cycle Time
Step 1 of 5
1
Prepare
2
Parts
3
Product
4
Recipe
5
Results
See the Full Workflow
Annotate and save the product. Select the machine and product, then create
a recipe.
Follow the Sequence
After automatic configuration, check interference, run the simulation, and review the available cycle time.
Check Each Handoff
Identify the saved product, verified configuration, and simulation
results. Detailed operations follow in the next sections.
3D Concept Illustration
Notes: {"使用者母版頁": 10, "原教材頁": 10, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "以概念圖串起標註→保存產品→選擇機台與產品→全自動配置→確認干涉→模擬→取得並判讀CT，不呈現操作動作；概念動畫不取代實測證據。", "未補齊證據": ["QS01-GAP-01", "G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 3
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 3 of 20
Page 17
Step 2 of 5
1
Prepare
2
Parts
3
Product
4
Recipe
5
Results
Open Component Search
01
New Single Board: check Board/BOM.
02
Select BOM to show the component list on the right.
03
Click + Add to insert a new item.
04
Click the new row's Part Number link to search components.
Fig. 1-01 Product and BOM
Fig. 1-02a New item and part number
Fig. 1-02b Add BOM item
Notes: {"使用者母版頁": 11, "原教材頁": 11, "整合單元來源頁": 138, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "維持一頁三段圖解：讀BOM／零件表→查候選→核對料號、照片、外形、尺寸與腳距；示範一個代表元件。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 4
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 4 of 20
Page 18
Step 2 of 5
1
Prepare
2
Parts
3
Product
4
Recipe
5
Results
Check Geometry and Part Number
01
Shape, then part number.
02
Blue capacitor: 495-2473-3-ND.
03
Same geometry and part number: link directly.
Change the original number: edit it.
Keep both numbers: use Deep Clone.
Different geometry: create a new component.
Fig. 1-03 Check geometry, part number, and name
Notes: {"使用者母版頁": 11, "原教材頁": 11, "整合單元來源頁": 139, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "維持一頁三段圖解：讀BOM／零件表→查候選→核對料號、照片、外形、尺寸與腳距；示範一個代表元件。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 5
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 5 of 20
Page 19
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Create the Board
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Product → New Single Board. Name the root TestBoard; click OK.
02
Right-click the board root → Create Geometry Link. Select Top Layer (Gerber) and click OK. Repeat for the 3D shape.
Fig. 1-04 Create the board
Fig. 1-05 Gerber and 3D links
Notes: {"使用者母版頁": 12, "原教材頁": 12, "整合單元來源頁": 147, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "同頁串起板件結構識別、Gerber匯入與圖層核對，以結果圖確認本次來源。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 6
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 6 of 20
Page 20
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Import Gerber
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Gerber link → Import Gerber Shape. In APEX, Ctrl-select the four Gerber files; click Open. Check the imported layers.
02
Right-click the board root → Focus View. Use the mouse wheel to adjust zoom.
Fig. 1-06 Import Gerber
Fig. 1-07 Focus on the board
Notes: {"使用者母版頁": 12, "原教材頁": 12, "整合單元來源頁": 148, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "同頁串起板件結構識別、Gerber匯入與圖層核對，以結果圖確認本次來源。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 7
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 7 of 20
Page 21
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Add BOM Items
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
BOM → Add. Click the new part-number link to search.
02
Link 495-2473-3-ND from the user database; check BOM.
03
Double-click the new designator, enter C52, and press Enter. Repeat for the other training items.
Fig. 1-08 BOM item
Fig. 1-08a Link the part number
Fig. 1-09 Designator
Notes: {"使用者母版頁": 14, "原教材頁": 14, "整合單元來源頁": 149, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "以對照表串起BOM建立、元件連結與RY1／C170／D01／C26位置辨識，示範一筆後核對全部。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 8
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 8 of 20
Page 22
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Create Insertion Annotations
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Add Insertion Annotation; right-click → Continuous Edit.
02
Select Footprint. Box-select the target 2D features; release and check the blue outline.
03
Enter C52, matching the BOM. Click Edit; check Properties.
Fig. 1-10 Insertion type
Fig. 1-11 Box-select the footprint
Fig. 1-12 Annotation name
Drag to select. Hold Ctrl and drag again to deselect.
Tip
Notes: {"使用者母版頁": 15, "原教材頁": 15, "整合單元來源頁": 150, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "同頁完成選取、Footprint、標註及方向檢查，典型選错修正放在同一動作後。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 9
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 9 of 20
Page 23
Step 3 of 5
1
Prepare
2
Parts
3
Product
4
Recipe
5
Results
Add Fiducials
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Add Fiducial Annotation; right-click → Continuous Create.
02
Enter FID1; select its Gerber feature and click Create. Repeat for FID2. Click Cancel to finish.
Fig. 1-13 Add a fiducial item
Fig. 1-14 Create two fiducials
Notes: {"使用者母版頁": 16, "原教材頁": 16, "整合單元來源頁": 152, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "同頁看四位置結果與必要光學點，確認加工與定位資料完整。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 10
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 10 of 20
Page 24
Step 3 of 5
1
Prepare
2
Parts
3
Product
4
Recipe
5
Results
Preview Components
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Click Component Preview. After loading, check model-to-annotation alignment.
Fig. 1-15 Preview components
Notes: {"使用者母版頁": 17, "原教材頁": 17, "整合單元來源頁": 151, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "以產品可用為目標，整合Payload Preview、名稱／型錄／預覽保存及Recipe可查找結果。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 11
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 11 of 20
Page 25
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Set the Board Geometry
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Geometry Link → Parametric Shape: select color; measure diagonal corners. Set L/W/H = 304.8/165/3 mm; Generate.
02
Exit Measure (click once and press Esc if needed). Right-click the top Gerber → Move. Set Z = 3.0 and click OK.
Fig. 1-16 Board geometry
Fig. 1-17 Height
Notes: {"使用者母版頁": 13, "原教材頁": 13, "整合單元來源頁": 153, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "用同一板件核對外形、Workpart尺寸及定位／安裝參考，確認正確編輯層級。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 12
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 12 of 20
Page 26
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Set Workpart Dimensions
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Workpart → Measure Diagonal: W/L/T = 165/304.8/3 mm.
Fig. 1-18 Set Workpart dimensions
Notes: {"使用者母版頁": 13, "原教材頁": 13, "整合單元來源頁": 154, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "用同一板件核對外形、Workpart尺寸及定位／安裝參考，確認正確編輯層級。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 13
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 13 of 20
Page 27
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Create the Board Mount Point
Designators: RY1, C172, D01, C52. Link each to its corresponding BOM part number.
01
Mount Points → Create Mount Point. Inspect Corner Mount Point.
Fig. 1-19 Default mount point
Notes: {"使用者母版頁": 13, "原教材頁": 13, "整合單元來源頁": 154, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "用同一板件核對外形、Workpart尺寸及定位／安裝參考，確認正確編輯層級。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 14
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 14 of 20
Page 28
Step 3 of 5
Prepare
Parts
Product
Recipe
Results
Save the Product
Use RY1, C172, D01, and C52. Match BOM designators, part numbers, and geometry before annotation.
01
Save: check name/version/path; add Product Catalog membership. Capture from 3D View; check preview, OK.
02
Recipe → Create Project: find the saved product. Demo_Single_Board is the completed reference.
Fig. 1-20 Save command and asset settings
Notes: {"使用者母版頁": 17, "原教材頁": 17, "整合單元來源頁": 155, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用單板操作範例；本次加工位置為 RY1、C170、D01、C26。", "目標": "以產品可用為目標，整合Payload Preview、名稱／型錄／預覽保存及Recipe可查找結果。", "未補齊證據": ["G-S1-PRODUCT"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 15
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 15 of 20
Page 29
Step 4 of 5
Prepare
Parts
Product
Recipe
Results
Select the Machine and Single-Board Product
Select your four-part single board. The panel illustrates the settings; use your product values.
01
Create Project: select the empty machine and saved four-part board; Next.
02
Check infeed, mount point, and conveyor width. Panel values are examples only.
Fig. 1-21 Create a recipe
Fig. 1-22 Product mounting
Notes: {"使用者母版頁": 18, "原教材頁": 18, "整合單元來源頁": 186, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用舊連板配方範例；本次選自己的四料單板，數量、尺寸與時間依實際結果。", "目標": "選機台與產品，核對方向、安裝參考及輸送寬度，同頁呈現組裝結果。", "未補齊證據": ["QS01-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 16
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 16 of 20
Page 30
Step 4 of 5
Prepare
Parts
Product
Recipe
Results
Mount the Product in the Machine
Fig. 1-22a Mounting position
Fig. 1-22b Orientation
Fig. 1-22c Attachment
Fig. 1-22d Conveyor width
Notes: {"使用者母版頁": 18, "原教材頁": 18, "整合單元來源頁": 186, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用舊連板配方範例；本次選自己的四料單板，數量、尺寸與時間依實際結果。", "目標": "選機台與產品，核對方向、安裝參考及輸送寬度，同頁呈現組裝結果。", "未補齊證據": ["QS01-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 17
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 17 of 20
Page 31
Step 4 of 5
Prepare
Parts
Product
Recipe
Results
Start Automatic Configuration
Select your four-part single board. The panel illustrates the settings; use your product values.
01
Remove unnecessary locks; click Automatic Configuration. Wait for completion.
02
Review the proposed feeders and tools. Click Import, read the prompt, and click Continue.
03
Wait for module import to finish. Check that configured positions turn green, required accessories are installed, and Next is available.
Fig. 1-23 Auto-configure
Fig. 1-24 Review and import setup
Notes: {"使用者母版頁": 19, "原教材頁": 19, "整合單元來源頁": 188, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用舊連板配方範例；本次選自己的四料單板，數量、尺寸與時間依實際結果。", "目標": "整合啟動、查看建議、匯入及完成狀態，不逐按鈕分頁。", "未補齊證據": ["QS01-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 18
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 18 of 20
Page 32
Step 4 of 5
Prepare
Parts
Product
Recipe
Results
Review the Process Flow
Check the components, tools, and operation sequence for your single-board product.
01
In Flow Editor, check designators, feeder/tool slots, and operation order.
Fig. 1-25 Process overview
Fig. 1-25a Tool / feeder steps
Fig. 1-25b Pickup order
Fig. 1-25c Insert order
Notes: {"使用者母版頁": 20, "原教材頁": 20, "整合單元來源頁": 189, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用舊連板配方範例；本次選自己的四料單板，數量、尺寸與時間依實際結果。", "目標": "核對Tool／Feeder與生成流程，執行必要規劃，保持自動配置結果。", "未補齊證據": ["QS01-GAP-01", "G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 19
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 19 of 20
Page 33
Step 4 of 5
Prepare
Parts
Product
Recipe
Results
Check Collisions and Simulation Controls
Check collisions, then run the simulation and review the cycle time.
01
Check collisions.
Grasp Pose: tool pose
Offset: adjust point
START: run
EXPORT DB: recipe
Fig. 1-26 Simulation controls
Fig. 1-27 Collision results
Notes: {"使用者母版頁": 20, "原教材頁": 20, "整合單元來源頁": 189, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用舊連板配方範例；本次選自己的四料單板，數量、尺寸與時間依實際結果。", "目標": "核對Tool／Feeder與生成流程，執行必要規劃，保持自動配置結果。", "未補齊證據": ["QS01-GAP-01", "G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 20
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 1 | Fully Automatic Single Board
Page 20 of 20
Page 34
Step 5 of 5
Prepare
Parts
Product
Recipe
Results
Initialize and Run the Simulation
Select your four-part single board. The panel illustrates the settings; use your product values.
01
Run Simulation; wait until Start is available.
02
Start; watch motion and CT until completion.
Fig. 1-28 Simulation in progress
Fig. 1-29 Export the D30 machine recipe
Notes: {"使用者母版頁": 21, "原教材頁": 21, "整合單元來源頁": 189, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用舊連板配方範例；本次選自己的四料單板，數量、尺寸與時間依實際結果。", "目標": "沿用同次未手動修改的配置模擬，觀察加工狀態，不先調整干涉。", "未補齊證據": ["QS01-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}