## Slide 1
1
2
3
4
5
Scenario 2: New Part Number, Same Geometry, Front-Side Feeding
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 1 of 18
Page 35
Step 1 of 5
Prepare
New Part
Update Product
Configure
Results
Updated Materials
Use the five-part BOM, part-number table, and the same board and Gerber data.
New Component Identity
C932-2123: same training shape/specs; different supplier and supplier part number.
On-Site Configuration Requirement
Install all feeders within the confirmed front-side area of the machine.
Notes: {"使用者母版頁": 23, "原教材頁": 23, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "一頁準備五料BOM／零件表、原元件、同一Gerber、目標位置及機台前側／槽位圖，說明新增C932-2123與供料限制。", "未補齊證據": ["G-S2-PART", "S2-GAP-02"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 2
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 2 of 18
Page 36
Step 1 of 5
1
Prepare
2
New Part
3
Update Product
4
Configure
5
Results
Quick Start: From a New Part to Front-Side Feeding
Component and Product
Use Deep Clone to create the new part. Update the existing product's links and annotations.
Configuration Strategy
Restrict the feeder area first, then let the algorithm configure the accessories.
Verification and Simulation
Check front-side feeding and interference, then simulate and review cycle time. This chapter focuses on the new part and area constraints.
Notes: {"使用者母版頁": 24, "原教材頁": 24, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用圖示呈現新舊料、Deep Clone、既有產品新增連結與標註、保存、機台／產品、前側配置、干涉確認、模擬與CT；不含隱藏2.6／2.7。", "未補齊證據": ["G-S2-PART", "S2-GAP-03", "G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 3
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 3 of 18
Page 37
Step 2 of 5
1
Prepare
2
New Part
3
Update Product
4
Configure
5
Results
Open Deep Clone
Use C932-2123 in place of the example part number. Keep it consistent across groups.
01
New Component → Deep Clone from Asset.
02
Set Group to All Groups. Browse the thumbnails, select the blue rectangular capacitor, and click OK.
Fig. 2-01d Select geometry
Fig. 2-01a Open Electronic Component
Fig. 2-01b Deep Clone
Fig. 2-01c All Groups
Notes: {"使用者母版頁": 26, "原教材頁": 26, "整合單元來源頁": 142, "每頁建議分鐘": "3–5", "來源界線": "本情境新料號為 C932-2123；畫面中的 495-2473-4 是舊操作範例。", "目標": "核對原元件後Deep Clone，設定新名稱與C932-2123，確認沒有覆寫原件。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 4
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 4 of 18
Page 38
Step 2 of 5
Prepare
New Part
Update Product
Configure
Results
Set the New Name and Group Part Numbers
Use C932-2123 in place of the example part number. Keep it consistent across groups.
01
Set the asset name and both group part numbers to C932-2123; click OK.
02
Read the Deep Clone from Asset reminder and click OK to return to the cloned asset editor. The preview and project file still require an initial save.
Fig. 2-01e New part number
Fig. 2-01f Clone completed
Notes: {"使用者母版頁": 26, "原教材頁": 26, "整合單元來源頁": 143, "每頁建議分鐘": "3–5", "來源界線": "本情境新料號為 C932-2123；畫面中的 495-2473-4 是舊操作範例。", "目標": "核對原元件後Deep Clone，設定新名稱與C932-2123，確認沒有覆寫原件。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 5
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 5 of 18
Page 39
Step 2 of 5
Prepare
New Part
Update Product
Configure
Results
Add AMBU Component Properties
Use C932-2123 in place of the example part number. Keep it consistent across groups.
01
Right-click the cloned asset root → Add Asset Property → AMBU Component.
02
Select AMBU Component. On the right, set Component Name and Part Number to C932-2123.
Fig. 2-02c AMBU Component properties
Fig. 2-02d Part number
Fig. 2-02a Zoom to component
Fig. 2-02b Component Feature
Notes: {"使用者母版頁": 27, "原教材頁": 27, "整合單元來源頁": 144, "每頁建議分鐘": "3–5", "來源界線": "本情境新料號為 C932-2123；畫面中的 495-2473-4 是舊操作範例。", "目標": "核對必要群組料號及Component資料，保存新資產與預覽，使用欄位對照圖。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 6
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 6 of 18
Page 40
Step 2 of 5
Prepare
New Part
Update Product
Configure
Results
Save the Cloned Asset
Use C932-2123 in place of the example part number. Keep it consistent across groups.
01
Click Save to Library. Check the name, save location, and group part number. Under Preview, click Capture from 3D View. Verify the cloned capacitor geometry, then click OK.
Fig. 2-02f Save to library
Name: geometry asset name
Description: General information about the new component
Group Membership:
Add Internal Component Group and UIBU. Set the Member ID in both groups to C932-2123.
Fig. 2-02e Capture from 3D
Fig. 2-02g Saved
Notes: {"使用者母版頁": 27, "原教材頁": 27, "整合單元來源頁": 145, "每頁建議分鐘": "3–5", "來源界線": "本情境新料號為 C932-2123；畫面中的 495-2473-4 是舊操作範例。", "目標": "核對必要群組料號及Component資料，保存新資產與預覽，使用欄位對照圖。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 7
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 7 of 18
Page 41
Step 3 of 5
Prepare
New Part
Update Product
Configure
Results
Open the Existing Product and Link the New Part
Use C932-2123 in place of the example part number. Keep it consistent across groups.
01
Open Demo_Single_Board. Add a BOM item and click its part-number link. Find and link C932-2123 in the user database.
02
Keep the original four parts. Add the fifth designator; check the updated list and Gerber location.
Fig. 2-03 Find part in BOM
Notes: {"使用者母版頁": 28, "原教材頁": 28, "整合單元來源頁": 146, "每頁建議分鐘": "3–5", "來源界線": "本情境新料號為 C932-2123；畫面中的 495-2473-4 是舊操作範例。", "目標": "確認新舊料號並存，Product能找到新料，未驗證的重開結果不宣稱完成。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 8
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 8 of 18
Page 42
Step 3 of 5
Prepare
New Part
Update Product
Configure
Results
Update Product Links and Annotations
Open Demo_Single_Board
Check the original four-part BOM links and annotations. Retain the existing content.
Add a Product Part-Number Link
Add C932-2123 and identify a suitable additional location in the same Gerber data.
Create the New Product Annotation
Box-select the footprint for the confirmed designator and check its orientation.
Fig. 2-04a Import BOM
Fig. 2-04b Column mapping
Fig. 2-04c Imported BOM
Fig. 2-04d Annotations
Notes: {"使用者母版頁": 29, "原教材頁": 29, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "開啟既有Demo_Single_Board，核對原四料及標註，於產品新增並連結C932-2123，再完成新增位置的產品標註；保留原四料標註，TBD位置必須先依Gerber核對。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 9
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 9 of 18
Page 43
Step 3 of 5
Prepare
New Part
Update Product
Configure
Results
Preview and Save the Five-Part Product
Save the Updated Version
Use a clear name and version with the latest preview. After saving, find the product in Recipe.
Fig. 2-05a Save to Library and name the product
Fig. 2-05b Add the product to Product Catalog
Fig. 2-05c Capture preview and save
Notes: {"使用者母版頁": 30, "原教材頁": 30, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "以整體結果核對原四料與新增料，完成預覽與保存。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 10
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 10 of 18
Page 44
Step 4 of 5
Prepare
New Part
Update Product
Configure
Results
Confirm the Machine Front and Allowed Area
Understand the Site Requirement
Constraints
Feeders: front-side slots 1–16 only.
Tools: front-side slots 1–4.
Learn the Software Settings
Apply settings that meet the
current constraints.
Fig. 2-06 Machine slots
Notes: {"使用者母版頁": 31, "原教材頁": 31, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用前側照片與槽位對照圖說明可用區域，不把舊槽號當作前後側證據。", "未補齊證據": ["S2-GAP-02"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 11
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 11 of 18
Page 45
Step 4 of 5
Prepare
New Part
Update Product
Configure
Results
Select the Machine and Updated Product
Select the product first, then set loading conditions. Feeder-area restrictions follow in the next steps.
01
In Recipe → Create Project, select the empty machine and the saved Demo_Single_Board_New.
Fig. 2-07 New project
Notes: {"使用者母版頁": 32, "原教材頁": 32, "整合單元來源頁": 179, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用載具配置範例；本次以五料產品與現場前側槽位對照圖為準。", "目標": "選更新產品建立Recipe，確認指定槽位為空後鎖定不可用區域，說明Lock保留當前狀態。", "未補齊證據": ["S2-GAP-02", "S2-GAP-03"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 12
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 12 of 18
Page 46
Step 4 of 5
Prepare
New Part
Update Product
Configure
Results
Mount the Product in the Machine
Fig. 2-08 Mounting
Notes: {"使用者母版頁": 32, "原教材頁": 32, "整合單元來源頁": 179, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用載具配置範例；本次以五料產品與現場前側槽位對照圖為準。", "目標": "選更新產品建立Recipe，確認指定槽位為空後鎖定不可用區域，說明Lock保留當前狀態。", "未補齊證據": ["S2-GAP-02", "S2-GAP-03"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 13
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 13 of 18
Page 47
Step 4 of 5
1
Prepare
2
New Part
3
Update Product
4
Configure
5
Results
Configuration Settings
Fig. 2-09a Keep slot 01 empty
Fig. 2-09b Slot 02 enabled, kept empty
Fig. 2-09c Use slot 07 with a Tube_3_box feeder for part 835-1A-F-V
Fig. 2-09d Slot 09 unlocked: the feeder can be reassigned
Notes: {"使用者母版頁": 32, "原教材頁": 32, "整合單元來源頁": 179, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用載具配置範例；本次以五料產品與現場前側槽位對照圖為準。", "目標": "選更新產品建立Recipe，確認指定槽位為空後鎖定不可用區域，說明Lock保留當前狀態。", "未補齊證據": ["S2-GAP-02", "S2-GAP-03"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 14
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 14 of 18
Page 48
Step 4 of 5
Prepare
New Part
Update Product
Configure
Results
Identify Slots That Must Remain Empty
Select the five-part product. Identify front-side slots on the machine layout and set the restrictions.
01
Open the feeder slots. Check the machine diagram; confirm front-side slots 1–16.
02
Verify the front/rear slot mapping. Lock prohibited empty slots; this example locks 17–32.
Fig. 2-10a Find empty slots
Fig. 2-10b Lock feeder slots
Fig. 2-10c Lock / unlock all slots
Notes: {"使用者母版頁": 32, "原教材頁": 32, "整合單元來源頁": 180, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用載具配置範例；本次以五料產品與現場前側槽位對照圖為準。", "目標": "選更新產品建立Recipe，確認指定槽位為空後鎖定不可用區域，說明Lock保留當前狀態。", "未補齊證據": ["S2-GAP-02", "S2-GAP-03"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 15
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 15 of 18
Page 49
Step 4 of 5
Prepare
New Part
Update Product
Configure
Results
Set the Tool Slot Restrictions
Select the five-part product. Identify front-side slots on the machine layout and set the restrictions.
01
Keep tool slots 1–4 available for this task.
02
Keep tool slots 1–4 available. Lock empty slots 5–8, then auto-configure.
Fig. 2-10d Lock empty tool slots
Fig. 2-10e Auto-configure within limits
Notes: {"使用者母版頁": 32, "原教材頁": 32, "整合單元來源頁": 181, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用載具配置範例；本次以五料產品與現場前側槽位對照圖為準。", "目標": "選更新產品建立Recipe，確認指定槽位為空後鎖定不可用區域，說明Lock保留當前狀態。", "未補齊證據": ["S2-GAP-02", "S2-GAP-03"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 16
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 16 of 18
Page 50
Step 5 of 5
Prepare
New Part
Update Product
Configure
Results
Check Interference, Then Simulate
Select the five-part product. Identify front-side slots on the machine layout and set the restrictions.
01
Next → Flow Editor. Check pick/insert order, then collisions.
02
Run Simulation; after initialization, click Start. Keep the cycle time and warnings for review.
Fig. 2-11 Setup and Flow Editor
Fig. 2-12 Check / simulate
Notes: {"使用者母版頁": 35, "原教材頁": 35, "整合單元來源頁": 184, "每頁建議分鐘": "3–5", "來源界線": "畫面沿用載具配置範例；本次以五料產品與現場前側槽位對照圖為準。", "目標": "同頁呈現流程與模擬結果，核對前側要求、加工範圍、CT與警告；操作引用已學方法。", "未補齊證據": ["S2-GAP-03", "G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 17
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 17 of 18
Page 51
Step 2 of 5
1
Prepare
2
New Part
3
Update Product
4
Configure
5
Results
Modify a Part Number
01
Internal database: find the original part and shape.
02
Add to User Database, or edit Part Number directly.
03
Set Part Number to 9999; verify.
04
Click Overwrite and confirm the successful database update message.
Fig. 2-13 Original part number and Overwrite
Fig. 2-14 Change the part number to 9999
Fig. 2-15 Successful update message
Notes: {"使用者母版頁": 25, "原教材頁": 25, "整合單元來源頁": 140, "每頁建議分鐘": "3–5", "來源界線": "延伸辨識：此功能會修改原料號；需要保留原料號時，請使用後續的深層複製。", "目標": "同頁對照相同規格／外形、不同製造商／料號，再圖解重用、修改、複製與新建的適用條件。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 18
DIATwin MachinePilot Training Kit
Scenario 2 | New Part and Front-Side Feeding
Page 18 of 18
Page 52
Step 2 of 5
1
Prepare
2
New Part
3
Update Product
4
Configure
5
Results
Verify the Update and Completion
This changes the original part number. To retain it, use Deep Clone as explained earlier in this chapter.
01
Return to the user database.
02
Find the edited blue capacitor. Check its new part number.
03
Completion Check
04
□ Geometry unchanged.
□ Part no.: 9999 or assigned.
□ Update confirmed.
□ Check part no. vs. asset name.
Fig. 2-16 The user database shows the new part number 9999
Notes: {"使用者母版頁": 25, "原教材頁": 25, "整合單元來源頁": 141, "每頁建議分鐘": "3–5", "來源界線": "延伸辨識：此功能會修改原料號；需要保留原料號時，請使用後續的深層複製。", "目標": "同頁對照相同規格／外形、不同製造商／料號，再圖解重用、修改、複製與新建的適用條件。", "未補齊證據": ["G-S2-PART"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}