## Slide 1
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 1 of 18
Page 71
Step 1 of 5
1
Prepare
2
No CAD
3
With CAD
4
Plan
5
Results
Scenario 4: Two Products on One Carrier
Shared starting data
Prepare Demo_Single_Board.
Without a CAD file
Create a simplified carrier from the required geometry and positioning data.
With a CAD file
Use pcb_holder.stp and the design reference for a separate example.
Notes: {"使用者母版頁": 51, "原教材頁": 58, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "一頁示意兩產品同一載具，列單板／四料表、装載圖及尺寸；有CAD路徑另備STEP及設計結果圖。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 2
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 2 of 18
Page 72
Step 2 of 5
Prepare
No CAD
With CAD
Plan
Results
Create a Carrier
01
Product → New Carrier. Name the root Carrier; click OK.
02
Carrier root → Open Project. Choose Demo_Single_Board from Product Catalog; click OK.
03
Repeat Open Project to load the same board again. Expand the tree and confirm that Demo_Single_Board and Demo_Single_Board_1 both exist.
Fig. 4-01. Create a carrier
Fig. 4-02 Load the single board twice
Notes: {"使用者母版頁": 53, "原教材頁": 60, "整合單元來源頁": 162, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "建立Carrier、載入兩個Board並配置第二板位置與方向，同頁依装載圖核對。", "未補齊證據": ["S4-GAP-01", "S4-GAP-02"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 3
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 3 of 18
Page 73
Step 2 of 5
Prepare
No CAD
With CAD
Plan
Results
Focus on the Objects
01
Carrier root → Focus Viewport.
02
Right-click Demo_Single_Board_1 → Move Board. Select Offset coordinates. Set X=330, Y=340, Z=0 mm, RX=0, RY=0, and RZ=180°. Click OK.
Fig. 4-03. Focus on the objects
Fig. 4-04 Second board position
Notes: {"使用者母版頁": 53, "原教材頁": 60, "整合單元來源頁": 163, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "建立Carrier、載入兩個Board並配置第二板位置與方向，同頁依装載圖核對。", "未補齊證據": ["S4-GAP-01", "S4-GAP-02"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 4
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 4 of 18
Page 74
Step 2 of 5
Prepare
No CAD
With CAD
Plan
Results
Create the Concept Geometry
01
Carrier root → Create 3D Link. Select Parametric Shape and Box.
02
Measure the layout's lower-left and upper-right corners; exit Measure.
03
Set color #4D4D4D; length 360, width 370, height 10 mm. Click Generate.
Fig. 4-05 Concept geometry
Fig. 4-06 Measure boards
Fig. 4-07 Carrier box
Note
Exit Measure: after the reference points and line appear, press Esc.
Notes: {"使用者母版頁": 54, "原教材頁": 61, "整合單元來源頁": 164, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "量測範圍後建立概念Box，量測圖、尺寸設定與外形結果同頁。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 5
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 5 of 18
Page 75
Step 2 of 5
Prepare
No CAD
With CAD
Plan
Results
Position the Two Boards
01
Board1,X = 30,Y = 15,Z = 10
02
Board2,X = 0.0,Y = 15,Z = 10
Fig. 4-08. Adjust both board heights
Fig. 4-09 Board offsets
Notes: {"使用者母版頁": 55, "原教材頁": 62, "整合單元來源頁": 165, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "用側視圖說明板件高度與載具位置，示範後確認相對關係，避免座標模式混用。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 6
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 6 of 18
Page 76
Step 2 of 5
Prepare
No CAD
With CAD
Plan
Results
Set Workpart Dimensions Without CAD
01
Select the carrier's Workpart properties and click Measure Diagonal. Select a lower corner and the diagonally opposite upper corner.
See the earlier chapter for details.
Alternatively, enter:
Width 370
Length 360
Thickness 10 mm
Fig. 4-10 Workpart dimensions
Notes: {"使用者母版頁": 56, "原教材頁": 63, "整合單元來源頁": 166, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "確認整體Workpart與預設定位點，不延伸Set Seat；列為優先試講頁。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 7
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 7 of 18
Page 77
Step 2 of 5
Prepare
No CAD
With CAD
Plan
Results
Save the Carrier
01
Save: check name/path/catalog. Capture from 3D View; OK. Confirm success.
02
Recipe → Create Project: find the saved carrier in Product.
Fig. 4-11 Save carrier
Notes: {"使用者母版頁": 57, "原教材頁": 64, "整合單元來源頁": 167, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "保存預覽與資產，核對兩板、外形、位置及高度，概念Box不是可製造性驗證。", "未補齊證據": ["S4-GAP-02"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 8
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 8 of 18
Page 78
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
Import STEP Geometry
The STEP carrier and the box carrier without CAD are separate examples with different dimensions. Check each independently.
01
Carrier geometry link → Import Shape from File.
02
Open Tutorials data/cad/pcb_holder.stp. Check the carrier geometry.
03
Select Hide Floor on the display toolbar at the left of the 3D rendering view.
Fig. 4-12a Remove geometry
02 Select the tutorial file
Fig. 4-12b Import STEP
Fig. 4-12c Select STEP file
Notes: {"使用者母版頁": 58, "原教材頁": 65, "整合單元來源頁": 168, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "獨立建立Carrier與Board，匯入pcb_holder.stp並確認外形，不繼承Box高度或位移。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 9
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 9 of 18
Page 79
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
Show and Hide the Floor
The STEP carrier and the box carrier without CAD are separate examples with different dimensions. Check each independently.
01
Carrier geometry link → Import Shape from File.
02
Open Tutorials data/cad/pcb_holder.stp. Check the carrier geometry.
03
Select Hide Floor on the display toolbar at the left of the 3D rendering view.
Fig. 4-13. Hide the floor
Fig. 4-13a. Before hiding
Fig. 4-13b Floor hidden
Notes: {"使用者母版頁": 58, "原教材頁": 65, "整合單元來源頁": 168, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "獨立建立Carrier與Board，匯入pcb_holder.stp並確認外形，不繼承Box高度或位移。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 10
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 10 of 18
Page 80
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
Move the Carrier Geometry
The STEP carrier and the box carrier without CAD are separate examples with different dimensions. Check each independently.
01
Geometry link → Move Geometry Link → Offset.
02
Set X=180.0, Y=185.0, Z=16.75 mm. Keep RX, RY, and RZ at 0 and click OK.
Fig. 4-14a Move Geometry Link
Fig. 4-14b. Set the carrier position
Notes: {"使用者母版頁": 59, "原教材頁": 66, "整合單元來源頁": 169, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "對照CAD及裝載要求，設定載具與板件位置、方向及高度，代表動作後核對整體。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 11
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 11 of 18
Page 81
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
Set Workpart Dimensions With CAD
The carriers with and without CAD are separate examples. Check their dimensions and positioning conditions independently.
01
Select Workpart at the carrier level. Confirm that the Properties panel refers to the current carrier.
02
Measure Diagonal: select opposite lower/upper corners. Check width 388, length 436, thickness 29.5 mm; enter thickness if needed.
Fig. 4-15 Workpart dimensions
Notes: {"使用者母版頁": 60, "原教材頁": 67, "整合單元來源頁": 170, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "量測整體尺寸後建立預設定位點，用同一模型圖確認厚度、位置Z與定位關係。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 12
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 12 of 18
Page 82
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
Create the CAD Carrier's Attachment Point
01
Right-click the carrier's attachment-point node and select Create Attachment Point.
02
Measure from the origin: click empty floor, then the carrier's machine contact point.
wcs_flr is the origin.
X=359.2, Y=−32.8, Z=14.5.
Enter these values as shown above.
Fig. 4-16 Attachment point
Notes: {"使用者母版頁": 60, "原教材頁": 67, "整合單元來源頁": 170, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "量測整體尺寸後建立預設定位點，用同一模型圖確認厚度、位置Z與定位關係。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 13
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 13 of 18
Page 83
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
CAD Carrier Attachment Point (Continued)
Fig. 4-16a Pick in 3D
Fig. 4-16b Set seat in 3D
Pick in 3D / Set Seat in 3D are not yet fully supported; verify the attachment point.
Notes: {"使用者母版頁": 60, "原教材頁": 67, "整合單元來源頁": 170, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "量測整體尺寸後建立預設定位點，用同一模型圖確認厚度、位置Z與定位關係。", "未補齊證據": ["S4-GAP-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 14
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 14 of 18
Page 84
Step 3 of 5
Prepare
No CAD
With CAD
Plan
Results
Set the Save Information
The STEP carrier and the box carrier without CAD are separate examples with different dimensions. Check each independently.
01
Save New_Carrier_Step: check path/catalog; Capture from 3D View, then OK.
02
Check the saved name in the success message. Click OK.
03
Select Recipe → Project Creation → Create Project. Find New_Carrier_Step or your chosen name in the Product list.
Fig. 4-17 Save STEP carrier
Notes: {"使用者母版頁": 61, "原教材頁": 68, "整合單元來源頁": 171, "每頁建議分鐘": "3–5", "來源界線": "有圖檔案例採用 STEP 載具；其尺寸與無圖檔方塊案例不同，分別核對。", "目標": "保存名稱、型錄與預覽，核對成功訊息及本案身分。", "未補齊證據": ["S4-GAP-02"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 15
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 15 of 18
Page 85
Continue from Carrier Product to Recipe
Select the product
Find the concept or STEP carrier by its saved name.
Processing data
Check the four processing locations on each board and the required positioning references.
Machine requirements
Check assembly conditions and supported feeders and tools. Learners plan the recipe independently.
Step 4 of 5
1
Prepare
2
No CAD
3
With CAD
4
Plan
5
Results
Notes: {"使用者母版頁": 63, "原教材頁": 70, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "確認載具可選取，核對加工位置、機台與配件依賴，完成產品自檢；不重教完整Recipe。", "未補齊證據": ["S4-GAP-02", "S4-EXT-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 16
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 16 of 18
Page 86
Step 4 of 5
Prepare
No CAD
With CAD
Plan
Results
Final Exercise: Select the Attachment Point
Incorrect fit; point hidden
Step 3:
SETTING IN 3D WORLD.
Pick points to align with the conveyor.
Notes: {"使用者母版頁": 64, "原教材頁": 71, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "一頁任務卡與三策略圖：全自動、指定配件／槽位、限制區域後自動，學員擇一完成。", "未補齊證據": ["S4-EXT-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 17
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 17 of 18
Page 87
Step 4 of 5
Prepare
No CAD
With CAD
Plan
Results
Final Exercise: Choose a Configuration Strategy
A: Fully automatic planning
Let the system select supported accessories and available positions.
B: Specify accessories and slots
Specify compatible modules and supported slots, then plan the process.
C: Auto-configure within an area
Lock unavailable empty slots and let the algorithm use the permitted area. Complete one strategy with your own carrier.
Notes: {"使用者母版頁": 64, "原教材頁": 71, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "一頁任務卡與三策略圖：全自動、指定配件／槽位、限制區域後自動，學員擇一完成。", "未補齊證據": ["S4-EXT-01"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}

## Slide 18
1
2
3
4
5
DIATwin MachinePilot Training Kit
Scenario 4 | Carrier and Final Outcome
Page 18 of 18
Page 88
Step 5 of 5
Prepare
No CAD
With CAD
Plan
Results
Run the Simulation and Explain the Results
Check interference first
Record the collision status and conditions that need attention.
Run the recipe
Simulate with the same product and configuration. Observe progress and completion.
Obtain different cycle-time results
Record the available cycle time, warnings, and unfinished items.
Notes: {"使用者母版頁": 66, "原教材頁": 73, "整合單元來源頁": null, "每頁建議分鐘": "3–5", "來源界線": "", "目標": "說明實作需執行與記錄的模擬、警告、CT及實際狀態；完整運算與作業另排。", "未補齊證據": ["S4-EXT-01", "G-CHECK"], "截圖處理": "保留真實介面；來源有文字帶者改用既有無文字帶出版截圖；單元局部圖沿用原圖裁切與來源。"}